## Slide 1
Arduino Alarm System
Guanglong Hu
GeoSc 597 Final Project
December 6nd, 2016

## Slide 2
Why Alarm System?
Experience of burglary
  Door is not locked
  People broke in the room at 2 am
Violence and crimes against specific ethic group
  “Meet the Flockers” by YG
  Fatal home invasion in Gwinnett County, Georgia
No AK-47 to protect myself

## Slide 3
Schematic of Alarm System
3
6
9
7
10
11
GND
5 V
GND
Echo
Trig
Vcc
Piezo Buzzer

## Slide 4
Devices
SR04-Ultrasonic Distance Measurement Sensor
Notes: GND and Vcc : connect to GND and 5 V, power supply
Trig: make the sensor to send sonar signal
Echo : read the signal back

## Slide 5
Devices
Distance Calculation
  At 20 degree C, speed of sound = 343.5 m/s = 0.03435 cm/ms
  Pace of sound = 1/speed of sound = 1/0.03435 = 29.1 ms/cm
  Duration = signal of Echo pin / 2
  Distance = Duration / Pace of Sound = Duration/29.1 = [cm]
  Code:
  int duration, distance;
  digitalWrite(trigPin, HIGH);
  delay(100);
  digitalWrite(trigPin, LOW);
  duration = pulseIn(echoPin, HIGH);
  distance = (duration/2) / 29.1;

## Slide 6
Devices
Piezo Buzzer

## Slide 7
State Machine Diagram
Start distance measurement
Send sonar signal, Green light on
Receive signal and calculate distance
Distance < 15 cm
Distance > 15 cm
Buzzer activated, flashing red and blue light

## Slide 8
Demonstration

## Slide 9
References
http://www.instructables.com/id/Using-a-SR04/
http://www.instructables.com/id/SIMPLE-ARDUINO-ULTRASONIC-SENSOR-DOOR-ALARM-/
http://www.makeuseof.com/tag/how-to-make-a-simple-arduino-alarm-system/

## Slide 10
Thank you !
Questions?